## Slide 1: A Case for Heterogeneous Disk Arrays
Toni Cortes and Jesús Labarta
Departament d’Arquitectura de Computadors
Univeritat Politècnica de Catalunya - Barcelona

## Slide 2: Disk Arrays (RAIDs)
Group several disks
  Single address space
  High capacity
  Improved performance
  Low cost
Heterogeneous RAID
  Not all disks are equal
B0
B1
B2
B3
B4
B5
B6
B7
...

## Slide 3: Motivation
Heterogeneous disk arrays are becoming a common configuration
  Replacing a new disk
  Adding new disks
Current solution
  All disks are treated as equal
    No performance gain is obtained
    No capacity gain is obtained

## Slide 4: Objective
AdaptRaid0
  Block-distribution policy
  Take advantage of the goodies of each disk
Target Environment
  Scientific and general purpose
  Not multimedia
    Solutions have already been presented
    Very dependent on some characteristics
  Disk arrays level 0 (RAID0)
    Level 5 is under development

## Slide 5: Related Work
Multimedia Systems
  Random distribution with replication (Santos98)
  Policy based on logical disks (Zimmerman98)
  Use fast disk for hot data (Dan95)
  Differences:
    Large blocks, only reads, and sustained bandwidth
General purpose
  HP AutoRaid (Wilkes95)
  Disc-Cache Disk (Hu98)
  Differences:
    Do not adapt to the existent hardware

## Slide 6: Disk Arrays and Parallelism
Parallelism within a request
  Requests have to large
    The sub-request of each disk has to be large
    Seek + search + transfer in all disks
Parallelism between requests
  The number of disks has to be large
    Compared to the average number of disks used in a requests

## Slide 7: AdaptRaid0: An Example
Basic idea
  Load each disk depending on its characteristics
Example
  1 fast disk
    Size = S
    Performance = P
  1 slow disk
    Size = S/2
    Performance = P/2
00
02
04
06
08
09
10
11
01
03
05
07
Fast
Slow
00
02
04
05
06
08
10
11
01
03
07
09
Fast
Slow
Patern

## Slide 8: AdaptRaid0: The Parameters
Utilization factor (UF)
  One factor per disk
    Larger disks have more blocks?
    Faster disks have more blocks?
Lines in pattern (LIP)
  We define a pattern using the UF
    Large patterns allow more requests with good disks
    Small patterns allow a better distribution

## Slide 9: AdaptRaid0: The Algorithm
Algorithm
  Decide LIP and Ufd
  Compute number of blocks per disk in the pattern
    Blocksd= int(UFd * LIP)
  Distribute blocks in a round-robin way
    Use the available disks
    A disk becomes unavailable when Blocksd have already been placed in it
  Repeat step 3 until one disk becomes full

## Slide 10: Methodology
Parameters
  UF based on the size of the disk
  Lines in pattern
    100 lines for 8-disk arrays
    10 lines for 32-disk arrays
Simulation
  Simulator: HRaid (Cortes99)
  Workload from HP labs (1999)
Reference systems
  Raid0 and OnlyFast

## Slide 11: Environment
Disks
  Fast disk
    Seagate Barracuda 4LP (4.339 Gbytes)
  Slow disk
    Seagate Cheetah 4LP (2.061 Gbytes)
Bus
    10us latency
    100Mbit/s bandwidth
File system
    10 requests in parallel

## Slide 12: Capacity Evaluation
Raid0
  Constant capacity
    Small
OnlyFast
  Small capacity with few disks
AadaptRaid0
  Offers the best size

## Slide 13: Performance Evaluation (8 disks)
Raid0
  Does not use
    Characteristics of good disks
OnlyFast
  Does not use
    Parallelism between requests

## Slide 14: Performance Evaluation (32 disks)
Raid0
  Does not use
    Characteristics of good disks
  It uses
    Parallelism between requests
OnlyFast
  Does not use
    Parallelism between requests

## Slide 15: Conclusions
AdaptRaid0
  Performance
    It knows how to use the disks
    Allows parallelism
  Size
    It uses all the available capacity

## Slide 16: Future Work
Solve the same problem for Raid5
  Problem of parity blocks
  Less scalable
    No parallelism among requests